## Slide 1: DEVICE FOR ENDANGERED SPECIES
By,
Pavithra VG
( B.E. Electronics and Communication Engineering )
(A Smart Collar Prototype for Wildlife Monitoring)

## Slide 2: Abstract
Problem Statement:
Need for a Tech-Based Collar
A smart collar integrates sensors, GSM, and GPS to continuously track animal health and location.
Provides real-time alerts to authorities, helping in faster intervention.
Enables conservationists to study migratory patterns, habitat usage, and health status with accurate data.
  Many endangered species face extinction due to poaching, habitat destruction, and lack of real-time monitoring.
  Manual monitoring is labor-intensive, costly, and provides limited coverage.

## Slide 3: Objectives
Monitor heartbeat (pulse sensor) and motion (PIR sensor) in real-time.
Trigger alerts when abnormal conditions are detected.
Send SMS alerts via GSM containing GPS location of the animal.
Assist in preventing poaching, illegal trade, and habitat threats.
Provide continuous data for research on animal behavior and conservation.

## Slide 4: Literature Survey
Existing Methods
Manual monitoring → time-consuming, limited coverage.
Radio/GPS collars → track location but costly & need expertise.
ZigBee systems → health monitoring but complex hardware.
Disadvantages
Labor & time intensive.
High cost of devices.
Limited real-time alerts.

## Slide 5: Proposed System
Key Components Integrated
A wearable smart collar built using Arduino UNO as the control unit.
Continuously monitors health (heartbeat sensor) and activity (PIR sensor).
On detecting abnormalities, it communicates through GSM and attaches GPS coordinates in the alert message.
Compact design ensures comfort and long-term usage
System Overview
Pulse Sensor → measures heartbeat.
PIR Sensor → detects motion of the animal or surrounding activity.
GSM Module → sends SMS alerts to authorities.
GPS Module → provides real-time location tracking.
Arduino UNO → processes sensor data and controls communication

## Slide 6: Block Diagram

## Slide 7: Hardware & Software Components
Hardware
Software
Arduino UNO – main controller
Pulse Sensor – monitors heartbeat
PIR Sensor – detects animal motion
GSM Module (SIM800L) – sends SMS alerts
GPS Module – provides real-time location
LED + Resistor – alert indicator
Silicon Belt – wearable collar base
Breadboard & Wires – circuit connections
Arduino IDE – coding & debugging
Blynk IoT – remote monitoring & mobile dashboard

## Slide 8: Hardware Setup
ARDUINO
PIR SENSOR
PULSE SENSOR
GSM
GSM MODULE

## Slide 9: Working Principle
Sensors (Pulse + PIR) continuously monitor animal health and movement.
When abnormal pulse or suspicious motion is detected:
LED blinks as a local alert indicator
Authorities receive real-time info → enabling quick action against threats like poaching or habitat risk.
Arduino processes the signals.
GSM module sends an SMS alert to authorities.
GPS module attaches the exact location.

## Slide 10: Code Snippet
int pirValue = digitalRead(PIR_PIN);
int heartRate = pulseSensor.getBeatsPerMinute();
float objTemp = mlx.readObjectTempC();
if (pirValue == HIGH || heartRate > 100 || objTemp > 38.0) {
Serial.println("⚠ ALERT: Abnormal condition detected!");
gsmSerial.println("AT+CMGS=\"+91XXXXXXXXXX\"");
gsmSerial.println("Animal in danger! Sending GPS...");

## Slide 11: Outputs
Arduino IDE Output

## Slide 12: Applications
AI Integration – Use machine learning to analyze sensor data and detect patterns more accurately.
Additional Sensors – Add temperature, humidity, and sound sensors for a holistic understanding of animal health and environment.
Data Fusion – Combine multi-sensor data for deeper insights into species’ well-being and behavior.
Energy Efficiency – Explore low-power designs for longer operational life in the field.

## Slide 13: Future Enhancements
AI Integration – Use machine learning to analyze sensor data and detect patterns more accurately.
Additional Sensors – Add temperature, humidity, and sound sensors for a holistic understanding of animal health and environment.
Data Fusion – Combine multi-sensor data for deeper insights into species’ well-being and behavior.
Energy Efficiency – Explore low-power designs for longer operational life in the field.

## Slide 14: Conclusions
The device represents a major step forward in wildlife conservation, combining sensors, communication, and tracking for real-time protection.
Acts as a vigilant sentinel against poaching and habitat threats.
Has potential to grow further with AI, sensor fusion, and energy-efficient upgrades
Stands as a beacon of hope, offering a practical pathway for safeguarding endangered species and preserving biodiversity.
.